## Slide 1: Enhancing Odor Classification in E-Nose Systems
Resia Suvejda Kiliç
Master of science in computer engineering
Supervisor: Prof. dr bekir karlik
2025

## Slide 2: OVERVIEW
01 INTRODUCTION
02 MOTIVATION & PROBLEM
03 OBJECTIVE & CONTRIBUTION
04 DATASET
05 DATA PREPROCESSING
06 MODEL ARCHITECTURE
07 IMPLEMENTATION - BACKEND
07 IMPLEMENTATION - FRONTEND
08 RESULTS & COMPARISON
09 CONCLUSION & FUTURE WORK

## Slide 3: 01 Introduction
Odor Classification is the process of identifying gases based on sensor signals
Electronic Nose is a sensor array system mostly suited into a device that mimics the human olfactory system to detect and classify odors
Used in healthcare, food quality, environmental monitoring

## Slide 4: 02 Motivation & Problem
Limitations of Traditional Machine Learning Models:
Struggle with time-based changes in sensor signals
Cannot adapt to long-term sensor drift and changing patterns
Why Deep Learning is Needed:
Understands how different sensors respond together at the same time
Captures time sequences
Focuses on important contextual features within the signals
Sensor Drift
Sensor response weakens due to aging or temp.

## Slide 5: 03 Objective & Contribution
Propose a hybrid deep learning model combining CNN + LSTM + Transformer
Improve odor classification accuracy over time even when conditions are not ideal
Develop a desktop application for training, evaluation, and model comparison

## Slide 6: 04 Dataset
Gas Sensor Array Drift Dataset
13,910 samples
Collected for 36 months
6 gases (Ethanol, Ethylene, Ammonia, Acetaldehyde, Acetone, Toluene)
16 sensors (4x of each sensor) -> 128 features/sample

## Slide 7: 05 Data Preprocessing
Handle missing data by removing major issues and filling minor ones with estimated values
Normalization with StandardScaler by Scikit-learn
Changed shape to (Time, Sensors) to work with LSTM and Transformer models
Data augmentation to help the model learn to handle variations in real-world data
  Adding small random variations of Gaussian noise
  Moving the signal slightly forward or backward in time
  Scaling the signal’s strength
Data grouped in batches for some time after processing

## Slide 8: 06 Model architecture
Captures local signal patterns
Models how these patterns change over time
Uses attention to focus on the most important time segments
Combined, they improve accuracy and help the model adapt to sensor noise and drift

## Slide 9: 07 implementation - Backend
FastAPI handles training, evaluation, visualizations
Request: Epochs, Batch Size, LR, Model Name
Response: Metrics and Visuals of the Trained Model
Request: Model File from Local
Response: Metrics and Visuals of the Evaluated Model
Request: Model File from Local
Response: Natural language analysis based on metrics of model
Client
GUI
API
Backend
Request
Response

## Slide 11: 07 implementation - Frontend
PyQt5 GUI desktop app with:
  Inputs for hyperparameters (epochs, batch size, learning rate)
  User can train, evaluate and compare models
  Visual results: Loss/Accuracy curves, Confusion Matrix, Feature Importance
Use Case 1: Train New Model
Input Epochs, Batch Size, LR, Model Name
Start Training
Get Visualizations and Metrics
Load a model from files
Start Evaluating
Get Visualizations, Metrics and Analysis
Use Case 2: Evaluate Existing Model

## Slide 12
App at starting

## Slide 13
App after a model is trained (use case 1)

## Slide 14
App after a model is evaluated (use case 2)

## Slide 15: 08 Results & Comparison
CNN + Attention – basic attention mechanisms | Our model uses LSTM to remember time patterns + Transformer to catch big-picture info
LSTM + SVM Ensemble - limited by basic ML methods
CNN + Transformer - weaker at extracting complex features
Transformer with Domain Adaptation - less stable
Most values are diagonally aligned which means almost
all samples were used for the prediction

## Slide 16: 09 Conclusion & Future Work
Future Work
Improve drift correction techniques
Hyperparameter Optimization
Deploying the API and the app to Live for broader use
Adding new data uploading button in the GUI
Integration of interactive dashboards (e.g., via Dash)
Conclusion
Hybrid deep learning (CNN-LSTM-Transformer) handles complex odor patterns effectively
Strong for chemical sensing tasks with noisy, time-based sensor data
Our model achieves faster training and higher performance with greater precision and flexibility, making it better than other models and suited for real-world applications and future advancements

## Slide 17: Thank you for your attention!